## Slide 1
Front lights
10-48 VDC input
Embedded computer
(Intel NUC)+hubs
12-24 VDC input
Power
USB (via FTDI)
USB
(via FTDI)
Ethernet
PWM
Front R+L brushed
motors (NPC-T64)
AHRS
(SBG Ellipse-A)
USB powered
PC interface
(Pololu Maestro 24)
10-30 VDC input
Beacon+relay
(DFR00017)
USB powered
USB
GPS antenna
PoE adapter
12-24 VDC input
Wi-Fi Mesh 802.11s
(Ubiquiti Bullet M2)
PoE
Wi-Fi antenna
Electronics battery+
voltage converters
GPS
(Drotek Tiny RTK)
USB powered
USB
Front R+L motors
battery+shared switch
Rear R+L motors
battery+shared switch
Front R+L ESC
(Roboteq FDC3260)
+shared e-stop
8-60 VDC input
PWM
Rear R+L brushed
motors (NPC-T64)
Rear R+L ESC
(Roboteq FDC3260)
+shared e-stop
8-60 VDC input
Power
Power
Power
5 VDC input
PWM
USB (via FTDI)
Switch
USB powered
Ethernet
5/12/24/48 VDC output
3D lidar
(Velodyne VLP-16
Puck LITE)
9-18 VDC input
Ethernet
Digital
Voltage converter
(CC-BEC)
14-25 VDC input
5 VDC output
Power
Carrier box
Payload box
External devices
RC receiver/telemetry
(TBS Crossfire)
PWM
Digital
Camera
(AXIS M3066-V)+PoE
48 VDC input
Ethernet